## Slide 1: Testing with the LV-500
Tektronix LV-500
Built in 1989-1991
  I.e. Ancient technology!
  eBay is a good source for spare parts these days…
Specifically designed to be a stand-alone tester for ASICs
  I.e. More testing features than a basic logic analyzer

## Slide 2: What’s an ASIC Tester?
Ours is built on a Tektronix DAS 9200 logic analyzer platform
The main differences are in the test head, the pattern/error cards, and the Schmoo
  The test head has up to 256 bi-directional pins where each pin has programmable electronics
    voltage drive, current drive, voltage sense, etc.
  The pattern/error cards store and compare the test vectors at up to 50MHz
    fast for 1989!
  A Schmoo lets you run repeated tests while the tester alters one or two independent variables like threshold, delay, cycle length, voltage, etc.

## Slide 3: Flavors of LV500s
Common Features
  Test speeds up to 50MHz
  Up to 64,000 unique test vectors
  Network connection for uploading tests
    Thinlan ethernet
  8 Meg of RAM
  21 or 43 Meg hard drive
  5.25 floppy (1.2M floppy)

## Slide 4: Flavors of LV500s
LV514
  192 test channels (12 sectors)
    160 are usable (two sectors are bad)
  Pre-wired test card for class chips
  (should really be called LV513, but that’s a long story)
LV512
  128 test channels (8 sectors)
    All channels are usable
  Used mostly for tutorial purposes
    No pre-wired class chip test card yet…

## Slide 5: LV514

## Slide 6: LV512

## Slide 7: The Big Picture
1010010100100 1001000010100 1110101001110 1010100010011 0100100010001
DUT (Device Under Test)
Compare
11010100101010 11110101010101 00101001010100 10010100010101 01010010010101
Input Vector Table
Expected Output Vector Table
Actual
Output
Vectors
Pass/Fail Display
Expected Output
Vectors

## Slide 8: The More Detailed Picture
Conceptually this is simple, in practice there are lots of details…
  Define the input and expected-output vectors
    Can do this using your Verilog simulations
  Define which signals are inputs and outputs on your chip
  Define how those signals are mapped to tester channels
  Wire up the DUT card so that those channels map to your chip pins
  Define the timing and electrical characteristics of your test

## Slide 9: Three Essential Parts of a Test
A properly wired DUT (Device Under Test) card
  This electrically connects each of your chip pins to the correct tester channels
A properly configured LV-500
  Configure the timing of when inputs are applied, when outputs are checked, what the voltages and currents are, etc.
A complete set of test vectors
  Vectors are applied and checked on each cycle
  “Force data” are inputs to your chip
  “Compare data” are expected outputs from your chip

## Slide 10: Tester Channels
The 256 possible pins (channels) on the test head are grouped into 16 “sectors” labeled 0-f
  Each sector has 16 channels
  Labeled sector.channel (I.e. 0.2, d.3, a.c)
On each cycle, each channel may be either a “force” channel or a “compare” channel, but not both
  If you have bi-directional pins on your chip, you need to define which are inputs and which are outputs on each cycle!

## Slide 11: DUT Card
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F

## Slide 12: LV514 Usable Channels
1
2
4
5
6
7
8
9
A
B
C
D
E
F
3
0

## Slide 13: LV512 Usable Channels
1
2
4
5
6
7
8
9
A
B
C
D
E
F
3
0

## Slide 14: DUT Card Sectors & Channels

## Slide 15: DUT Cards
The DUT cards are how you wire from tester channels to chip pins
These cards also have VDD, VTT and GND power supply connections
  VDD and VTT are two independently controllable power supply voltages

## Slide 16: Wiring the DUT Card
Essentially two choices:
  Solder wires on a PGA DUT card
    Remember that VDD and GND are not connected to tester channels
    Probably only want to do this once for the whole class
    Which means standardizing VDD and GND!
  Use a “Quick-Connect” card
    Uses 3M Scotch-Connect to wire (using wire-wrap wire) from the tester channels to the chip socket
    Can also use quick-connect for VDD and GND

## Slide 17: Quick-Connect DUT Card

## Slide 18: Quick-Connect DUT Card

## Slide 19: Knowing What to Wire
A “Bonding Diagram” is a picture that shows how your chip was bonded to the chip frame
It also shows how the chip frame is connected to the chip pins

## Slide 20: Bonding/Chip Diagram

## Slide 21: Map Your Pins to Channels
Pick tester sector.channel assignments for each of your pins
  Signals that need the same voltage characteristics should be grouped in the same sector
    Each sector gets common voltage ranges
    More on this later…
  Signals that need the same timing should be grouped in the same quadrant
    Sectors 0-3, 4-7, 8-b, c-f are the four quadrants
    More on this later…
  Wire things up!
    Remember to keep a list of what you’ve wired!

## Slide 22: Class DUT Card
Pre-wired for class chips
  84 pin PGA with specific VDD and GND placements in the pad ring
  /usr/local/contrib/elb/lv500/DUTmap.txt

## Slide 23: DUTmap.txt
PAD-PIN-TESTER CHANNEL MAP FOR CS/EE 5710 DUT CARD
Pad locations are taken from MOSIS bonding diagram
PGA locations are taken from 84pin PGA bonding diagram
Tester channels 6,7,8,9,A are used. The notation is sector.channel
Vdd and GND connections are as per 5710 standard pad frame
TESTER SIGNAL
PAD PGA sec.chn NAME (no spaces)
---------------------------------
1 B02 6.C
2 C02 7.7
3 B01 6.B
4 C01 7.6
5 D02 7.D
6 D01 7.C
7 F02 GND GND
8 E02 8.1
9 E01 8.0
10 E03 8.7
12 F01 8.6
13 G01 8.A etc….

## Slide 24: Finished DUT Card
Now you have part 1 – a wired DUT card that connects your chip to the tester
On to part 2 – configuring the tester…

## Slide 25: LV512 Boot Menu

## Slide 26: LV500 Main Menu

## Slide 27: LV500 Keyboard Layout

## Slide 28: Important Menu Choices
Config Menu
  Defines voltages for VDD, VTT, GND
  Defines voltages for two force/compare sets
DUT Wiring menu
  Defines how your signals are assigned to tester sector.channels
Channel menu
  Defines how your signals are collected into groups (I.e. buses)
    ALL signals must be a part of some group
    Groups are assigned to specific timing templates (clock phases)

## Slide 29: Important Menu Choices
Template Menu
  Defines timing of tests
    When to force data?
    When to compare data
    When to ignore data?
Schmoo Menu
  Defines which variables to vary, and by how much
Pattern Menu
  Defines data vectors for each tester cycle

## Slide 30: Basic Procedure…
Tell tester which chip signals are connected to which channels (DUT wiring menu)
Combine signals into groups (Channel menu)
Define timing for each group (Template menu)
  Only four “clock phases” per quadrant
  A “template” assigns clock phases to groups, and timing of clock phases…
Define patterns (Pattern menu)
  Each pattern starts with a template
  Includes force, compare, and mask data for each test cycle

## Slide 31: Config Menu
Defines the electronics for this test
  VDD, VTT, GND, current limit, etc.
You can also define two different “force” and “compare” voltage sets for data channels
  Each sector uses one of these two sets

## Slide 32: Config Menu (diagram)

## Slide 33: Config Menu (LV512)

## Slide 34: DUT Wiring Menu
Defines how your signals are assigned to tester sector.channels
  List signal names
  Define which tester channels they connect to
  Optionally define which actual chip (DUT) pins they are connected to
    This is just a comment for documentation

## Slide 35: DUT Wiring Menu

## Slide 36: Channel Menu
Defines how your signals are collected into groups
EVERY signal must be a part of some group (even single signals)
  Groups can make data entry and evaluation easier
  Can define how group data is printed
    Dec, Hex, Oct, Bin
  Can specify timing once for the whole group
  In general, inputs vs. outputs is a good group…
    Or control vs. data, etc.

## Slide 37: Channel Menu (LV500)

## Slide 38: Channel Menu (LV500)

## Slide 39: Templates
Templates
  Defines timing of tests
    When to force data?
    When to compare data
    When to ignore data?
  Set up using a “clock phase”
    Bad name – really a timing waveform
    Defines when things happen in each tester cycle
  You can define up to four clock phases per quadrant

## Slide 40: Clock Phases
  Cycle Length: 20ns – 496ns
  Delay is delay to Leading Edge
    Can be 0ns
  Width is delay from Leading to Trailing edge

## Slide 41: DUT Card Quadrants
Each quadrant has up to four timing waveforms you can use to control signal timing (called “Clock Phases” in LV500-speak)

## Slide 42: Force Formats
  Within a clock phase, you can define when values are “forced” to your chip in relation to the edges

## Slide 43: Force Formats Example
  This is an example of a pattern driven on five consecutive tester cycles with each of the different force formats

## Slide 44: Compare Formats
  You can also define when you Compare outputs in relation to the clock phase edges

## Slide 45: Template Menu

## Slide 46: Pattern Menu
Defines data vectors for each tester cycle
  Data for each signal is defined in the data vector
  Some of those signals are “Force”, some are “Compare” and some are “Mask”
    These are set in the templates
    Assign a template to each vector
    On each tester cycle, the next vector, with that vector’s template, is applied to the DUT and compared

## Slide 47: Pattern Menu

## Slide 48: Pattern Display
The Pattern screen is where you see the results of your test
  Before the test you can see all the vectors (and their templates) that you will be using
  After running the test you see the same display with any errors highlighted in red
    Red means that the output of the DUT didn’t match the expected output vector
  You run the test with F1-Start (the F1 function key)

## Slide 49: Successful Test

## Slide 50: Failed Test

## Slide 51: Schmoo Menu
After you have your basic test working, you can run a Schmoo test
  Repeat the test while changing 1 or 2 variables
    Variables can be things like VDD voltage, delay time, cycle time. Compare voltage, etc.
  Generates a graph showing where the part worked or didn’t work

## Slide 52: Schmoo Menu

## Slide 53: Schmoo Result

## Slide 54: Logistics
The LV500 is old and cranky…
  Basic rule – if you’re not SURE about what you’re doing, ask me first!!!!
    Replacement parts are very hard (impossible?) to find.
  Leave terminal ON
    Turn down brightness when you leave,
    Check brightness when you come into the lab
  Do NOT turn the LV500 off without good cause!
    We’ll leave the LV512 up and running for tutorials, and then switch to the LV514 when chips come back…

## Slide 55: Logistics continued
Be very gentle with the DUT cards
  They connect to the machine through elastomer connectors
    These are basically rubber-like connectors wrapped with wire
    They are very fragile, and a little worse for wear
    We have no replacements…
Schedule some time with me to run tests!
  Once you’ve got some LV500 time under you belt you can go it alone…

## Slide 56: Tester Setup Simplified
All this stuff can be defined in a .msa file
  Module Setup, Ascii
  Each section of the .msa file corresponds roughly to a tester menu
  You can (fairly easily) write your own .msa file
    Templates on /usr/local/contrib/elb/lv500/

## Slide 57: Tester Setup with msa Files
You can ftp to the lv500 and upload the .msa file which defines your test
  You can ONLY ftp from vlsi-nat.cs.utah.edu so ssh to there first!
  lv512.cs.utah.edu, lv514.cs.utah.edu
  No username/password required…
  Put your .msa file into the Simulation directory on the LV500
  Convert to tester setup using the LV Toolkit menu

## Slide 58: LV512 LAN Screen

## Slide 59: LV Toolkit Menu (LV512)

## Slide 60: LV Toolkit Issues
Note that the conversion process goes to an ms_04_4.msp file (or something close to that)
  You are not allowed to change this name!
  If you want to save this setup under a different name you need to convert to the standard name, and then save the setup to a new name using the Disk Services menu.
Once the .msa is converted, you can look at the setup using all the previous menus

## Slide 61: Running Tests
The .msa conversion is a great first step
  But, after that’s running you may want to change things or try new things
    Like Schmoo, or changing parameters
  You can change the data using the menus shown earlier
  You can also save the changed tests into new .msa files
  And you can retrieve those new .msa files using FTP if you like

## Slide 62: Overview
On every tester cycle the LV500:
  Applies a set of signals to the DUT
    The data to “Force” is defined in the Pattern
    Which signals are “Forced” on this cycle is defined in the template
    When the data are applied is defined relative to the “clock phase” template
    The names of the signals and which tester channels they are on are defined in the DUT wiring menu
  At the right time (defined in the template) the tester captures and compares the data from the DUT
    Compares against the data in the Pattern

## Slide 63: Procedure
Get your bonding diagram and map where your signals are on your chip
Decide how those pins will map to tester channels (DUTmap.txt)
Decide on timing templates for all signals
Generate test vectors that include pin names, templates, and data vectors for every cycle
Put it all in a .msa file

## Slide 64: Procedure 2
Upload the .msa file to the LV500
Convert the .msa file to a tester setup file
Check all menus to make sure things are how you want them
  Config
  DUT wiring
  Channel
  Template
  Pattern

## Slide 65: Procedure 3
Fix or modify test parameters
Run your test
Look at the results
  Celebrate!
  Or diagnose and debug…
  Or decide to schmoo to get more info…

## Slide 66: Tutorial DUT Card

## Slide 67: Tutorial 1: 74LS547
3 to 8 decoder

## Slide 68: 74LS547

## Slide 69: 547 DUT Wiring

## Slide 70: 547 Template

## Slide 71: 547 Pattern

## Slide 72: 547 Schmoo

## Slide 73: Tutorial 2: 74LS299
Shift Register, shift L or R, parallel load and output
  Bidirectional data bus

## Slide 74: 74LS299 Timing
Control should be set up ahead of the clock
Data should be sampled after the rising edge of the clock
Data should be driven after the control is set up
  Avoid drive fights on bidirectional path

## Slide 75: 74LS299 Timing
Control signals
Clock
Shift data
Cycle = 200ns
Delay = 0ns, Width = 100ns
Delay = 40ns, Width = 100ns
Delay = 20ns, Width = 80ns

## Slide 76: 74LS299 Shift/Clear Template

## Slide 77: 74LS299 Load Template

## Slide 78: 74LS299 Pattern